## Slide 1: CS/EE 217 GPU Architecture and Parallel Programming Lecture 10 Reduction Trees

## Slide 2: Objective
To master Reduction Trees, arguably the most widely used parallel computation pattern
  Basic concept
  Performance analysis
    Memory coalescing
    Control divergence
    Thread utilization

## Slide 3: Partition and Summarize
A commonly used strategy for processing large input data sets
  There is no required order of processing elements in a data set (associative and commutative)
  Partition the data set into smaller chunks
  Have each thread to process a chunk
  Use a reduction tree to summarize the results from each chunk into the final answer
We will focus on the reduction tree step for now.
Google and Hadoop MapReduce frameworks are examples of this pattern

## Slide 4: Reduction enables other techniques
Reduction is also needed to clean up after some commonly used parallelizing transformations
Privatization
  Multiple threads write into an output location
  Replicate the output location so that each thread has a private output location
  Use a reduction tree to combine the values of private locations into the original output location

## Slide 5: What is a reduction computation
Summarize a set of input values into one value using a “reduction operation”
  Max
  Min
  Sum
  Product
  Often with user defined reduction operation function as long as the operation
    Is associative and commutative
    Has a well-defined identity value (e.g., 0 for sum)

## Slide 6: An efficient sequential reduction algorithm performs N operations - O(N)
Initialize the result as an identity value for the reduction operation
  Smallest possible value for max reduction
  Largest possible value for min reduction
  0 for sum reduction
  1 for product reduction
Scan through the input and perform the reduction operation between the result value and the current input value

## Slide 7: A parallel reduction tree algorithm performs N-1 Operations in log(N) steps
3
1
7
0
4
1
6
3
3
7
4
6
max
max
max
max
max
max
7
6
max
7

## Slide 8: A tournament is a reduction tree
What is the reduction operation?

## Slide 9: A Quick Analysis
For N input values, the reduction tree performs
  (1/2)N + (1/4)N + (1/8)N + … (1/N) = (1- (1/N))N = N-1 operations
  In Log (N) steps – 1,000,000 input values take 20 steps
    Assuming that we have enough execution resources
  Average Parallelism (N-1)/Log(N))
    For N = 1,000,000, average parallelism is 50,000
    However, peak resource requirement is 500,000!
This is a work-efficient parallel algorithm
  The amount of work done is comparable to sequential
    Many parallel algorithms are not work efficient
  But not resource efficient…

## Slide 10: A Sum Reduction Example
Parallel implementation:
  Recursively halve # of threads, add two values per thread in each step
  Takes log(n) steps for n elements, requires n/2 threads
Assume an in-place reduction using shared memory
  The original vector is in device global memory
  The shared memory is used to hold a partial sum vector
  Each step brings the partial sum vector closer to the sum
  The final sum will be in element 0
  Reduces global memory traffic due to partial sum values

## Slide 11: Vector Reduction with Branch Divergence
0
1
2
3
4
5
7
6
10
9
8
11
0+1
2+3
4+5
6+7
10+11
8+9
0...3
4..7
8..11
0..7
8..15
1
2
3
Partial Sum elements
steps
Thread 0
Thread 4
Thread 1
Thread 2
Thread 3
Thread 5
Data

## Slide 12: A Sum Example
3
1
7
0
4
1
6
4
7
5
9
11
14
25
1
2
3
steps
Thread 0
Thread 1
Thread 2
Thread 3
Data
3
Active Partial Sum elements

## Slide 13: Simple Thread Index to Data Mapping
Each thread is responsible of an even-index location of the partial sum vector
  One input is the location of responsibility
After each step, half of the threads are no longer needed
In each step, one of the inputs comes from an increasing distance away

## Slide 14: A Simple Thread Block Design
Each thread block takes 2* BlockDim input elements
Each thread loads 2 elements into shared memory
  __shared__ float partialSum[2*BLOCK_SIZE];
  unsigned int t = threadIdx.x;
  unsigned int start = 2*blockIdx.x*blockDim.x;
  partialSum[t] = input[start + t];
  partialSum[blockDim+t] = input[start+ blockDim.x+t];

## Slide 15: The Reduction Steps
  for (unsigned int stride = 1;
  stride <= blockDim.x; stride *= 2)
  {
  __syncthreads();
  if (t % stride == 0)
  partialSum[2*t]+= partialSum[2*t+stride];
  }
Why do we need syncthreads()?

## Slide 16: Back to the Global Picture
Thread 0 in each thread block write the sum of the thread block in partialSum[0] into a vector indexed by the blockIdx.x
There can be a large number of such sums if the original vector is very large
  The host code may iterate and launch another kernel
If there are only a small number of sums, the host can simply transfer the data back and add them together.

## Slide 17: Some Observations
In each iteration, two control flow paths will be sequentially traversed for each warp
  Threads that perform addition and threads that do not
  Threads that do not perform addition still consume execution resources
No more than half of threads will be executing after the first step
  All odd-index threads are disabled after first step
  After the 5th step, entire warps in each block will fail the if test, poor resource utilization but no divergence.
    This can go on for a while, up to 5 more steps (1024/32=16= 25), where each active warp only has one productive thread until all warps in a block retire
  Some warps will still succeed, but with divergence since only one thread will succeed

## Slide 18: Thread Index Usage Matters
In some algorithms, one can shift the index usage to improve the divergence behavior
  Commutative and associative operators
Example - given an array of values, “reduce” them to a single value in parallel
  Sum reduction: sum of all values in the array
  Max reduction: maximum of all values in the array
  …

## Slide 19: A Better Strategy
Always compact the partial sums into the first locations in the partialSum[] array
Keep the active threads consecutive

## Slide 20: An Example of 16 threads
Thread 0
0
1
2
3
…
13
15
14
18
17
16
19
0+16
15+31
Thread 1
Thread 2
Thread 14
Thread 15

## Slide 21: A Better Reduction Kernel
  for (unsigned int stride = blockDim.x;
  stride > 0; stride /= 2)
  {
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t+stride];
  }

## Slide 22: A Quick Analysis
For a 1024 thread block
  No divergence in the first 5 steps
  1024, 512, 256, 128, 64, 32 consecutive threads are active in each step
  The final 5 steps will still have divergence

## Slide 23: A Story about an Old Engineer
From Hwu/Yale Patt

## Slide 24: Parallel Algorithm Overhead
  __shared__ float partialSum[2*BLOCK_SIZE];
  unsigned int t = threadIdx.x;
  unsigned int start = 2*blockIdx.x*blockDim.x;
  partialSum[t] = input[start + t];
  partialSum[blockDim+t] = input[start+ blockDim.x+t];
  for (unsigned int stride = blockDim.x/2;
  stride >= 1; stride >>= 1)
  {
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t+stride];
  }

## Slide 25: Parallel Algorithm Overhead
  __shared__ float partialSum[2*BLOCK_SIZE];
  unsigned int t = threadIdx.x;
  unsigned int start = 2*blockIdx.x*blockDim.x;
  partialSum[t] = input[start + t];
  partialSum[blockDim+t] = input[start+ blockDim.x+t];
  for (unsigned int stride = blockDim.x/2;
  stride >= 1; stride >>= 1)
  {
  __syncthreads();
  if (t < stride)
  partialSum[t] += partialSum[t+stride];
  }

## Slide 26: Parallel Execution Overhead
3
1
7
0
4
1
6
3
4
7
5
9
+
+
+
+
+
+
7
6
+
7
Although the number of “operations” is N, each “operation involves much more complex address calculation and intermediate result manipulation.
If the parallel code is executed on a single-thread hardware, it would be significantly slower than the code based on the original sequential algorithm.

## Slide 27: Any More QUESTIONS?