## Slide 1: CS/EE 217 GPU Architecture and Parallel Programming Lecture 15: Atomic Operations and Histogramming - Part 2

## Slide 2: Objective
To learn practical histogram programming techniques
  Basic histogram algorithm using atomic operations
  Privatization

## Slide 3: Review: A Histogram Example
In phrase “Programming Massively Parallel Processors” build a histogram of frequencies of each letter
A(4), C(1), E(1), G(1), …
How do you do this in parallel?
  Have each thread to take a section of the input
  For each input letter, use atomic operations to build the histogram

## Slide 4: Iteration #1 – 1st letter in each section
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
B
C
D
E
1
F
G
H
I
J
K
L
M
2
N
O
P
1
Q
R
S
T
U
V

## Slide 5: Iteration #2 – 2nd letter in each section
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
1
B
C
D
E
1
F
G
H
I
J
K
L
1
M
3
N
O
P
1
Q
R
1
S
T
U
V

## Slide 6: Iteration #3
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
1
B
C
D
E
1
F
G
H
I
1
J
K
L
1
M
3
N
O
1
P
1
Q
R
1
S
1
T
U
V

## Slide 7: Iteration #4
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
1
B
C
D
E
1
F
G
1
H
I
1
J
K
L
1
M
3
N
1
O
1
P
1
Q
R
1
S
2
T
U
V

## Slide 8: Iteration #5
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
1
B
C
D
E
1
F
G
1
H
I
1
J
K
L
1
M
3
N
1
O
1
P
2
Q
R
2
S
2
T
U
V

## Slide 9: What is wrong with the algorithm?
Reads from the input array are not coalesced
  Assign inputs to each thread in a strided pattern
  Adjacent threads process adjacent input letters
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
B
C
D
E
F
G
1
H
I
J
K
L
M
N
O
1
P
1
Q
R
1
S
T
U
V

## Slide 10: Iteration 2
P
R
O
G
R
A
M
M
I
N
G
M
A
V
I
S
S
Y
L
E
P
Thread 0
Thread 1
Thread 2
Thread 3
A
1
B
C
D
E
F
G
1
H
I
J
K
L
M
2
N
O
1
P
1
Q
R
2
S
T
U
V
All threads move to the next section of input

## Slide 11: A Histogram Kernel
The kernel receives a pointer to the input buffer
Each thread process the input in a strided pattern
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
int i = threadIdx.x + blockIdx.x * blockDim.x;
// stride is total number of threads
int stride = blockDim.x * gridDim.x;

## Slide 12: More on the Histogram Kernel
// All threads handle blockDim.x * gridDim.x
// consecutive elements
while (i < size) {
atomicAdd( &(histo[buffer[i]]), 1);
i += stride;
}
}

## Slide 13: Atomic Operations on DRAM
An atomic operation starts with a read, with a latency of a few hundred cycles

## Slide 14: Atomic Operations on DRAM
An atomic operation starts with a read, with a latency of a few hundred cycles
The atomic operation ends with a write, with a latency of a few hundred cycles
During this whole time, no one else can access the location

## Slide 15: Atomic Operations on DRAM
Each Load-Modify-Store has two full memory access delays
  All atomic operations on the same variable (RAM location) are serialized
DRAM delay
DRAM delay
transfer delay
internal routing
DRAM delay
transfer delay
internal routing
..
atomic operation N
atomic operation N+1
time

## Slide 16: Latency determines throughput of atomic operations
Throughput of an atomic operation is the rate at which the application can execute an atomic operation on a particular location.
The rate is limited by the total latency of the read-modify-write sequence, typically more than 1000 cycles for global memory (DRAM) locations.
This means that if many threads attempt to do atomic operation on the same location (contention), the memory bandwidth is reduced to < 1/1000!

## Slide 17: You may have a similar experience in supermarket checkout
Some customers realize that they missed an item after they started to check out
They run to the isle and get the item while the line waits
  The rate of check is reduced due to the long latency of running to the isle and back.
Imagine a store where every customer starts the check out before they even fetch any of the items
  The rate of the checkout will be 1 / (entire shopping time of each customer)

## Slide 18: Hardware Improvements (cont.)
Atomic operations on Fermi L2 cache
  medium latency, but still serialized
  Global to all blocks
  “Free improvement” on Global Memory atomics
internal routing
..
atomic operation N
atomic operation N+1
time
data transfer
data transfer

## Slide 19: Hardware Improvements
Atomic operations on Shared Memory
  Very short latency, but still serialized
  Private to each thread block
  Need algorithm work by programmers (more later)
internal routing
..
atomic operation N
atomic operation N+1
time
data transfer

## Slide 20: Atomics in Shared Memory Requires Privatization
Create private copies of the histo[] array for each thread block
__global__ void histo_kernel(unsigned char *buffer,
long size, unsigned int *histo)
{
__shared__ unsigned int histo_private[256];
if (threadIdx.x < 256) histo_private[threadidx.x] = 0;
__syncthreads();

## Slide 21: Build Private Histogram
int i = threadIdx.x + blockIdx.x * blockDim.x;
// stride is total number of threads
int stride = blockDim.x * gridDim.x;
while (i < size) {
atomicAdd( &(histo_private[buffer[i]), 1);
i += stride;
}

## Slide 22: Build Final Histogram
// wait for all other threads in the block to finish
__syncthreads();
if (threadIdx.x < 256)
atomicAdd( &(histo[threadIdx.x]), histo_private[threadIdx.x] );
}

## Slide 23: More on Privatization
Privatization is a powerful and frequently used techniques for parallelizing applications
The operation needs to be associative and commutative
  Histogram add operation is associative and commutative
The histogram size needs to be small
  Fits into shared memory
What if the histogram is too large to privatize?

## Slide 24: Other Atomic operations
atomicCAS (int *p, int cmp, int val)
  CAS = compare and swap
    //atomically perform the following
    int old = *p;
    if(cmp == old) *p = v;
    return old;
AtomicExch – unconditional version of CAS
    int old = *p;
    *p = v;
    return old
What are these used for?

## Slide 25: Locking causes control divergence in GPUs
Divergence deadlock if locking thread idles

## Slide 26: Alternatives to locking?
Lock-free algorithms/data structures
  Update a private copy
  Try to atomically update a global data structure using compare and swap or similar
  Retry if failed
  Need data structures that support this kind of operation
Wait-free algorithms/data structures
  Similar to histogramming – don’t wait, but atomic update
  But applies only to some algorithms

## Slide 27: Lock free vs. locking
Example from Nvidia presentation at GTC 2013

## Slide 28: Parallel Linked List Example

## Slide 32: ANY MORE QUESTIONS?