## Slide 1: CS/EE 217 GPU Architecture and Parallel Programming Lectures 4 and 5: Memory Model and Locality

## Slide 2: Objective
To learn to efficiently use the important levels of the CUDA memory hierarchy
  Registers, shared memory, global memory
  Tiled algorithms and barrier synchronization

## Slide 3: The Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 4: Going back to the program
Every instruction needs to be fetched from memory, decoded, then executed.
  The decode stage typically accesses register file
Instructions come in three flavors: Operate, Data transfer, and Program Control Flow.
An example instruction cycle is the following:
Fetch | Decode | Execute | Memory
Notes: victoria@samsung.com

## Slide 5: Operate Instructions
Example of an operate instruction:
ADD R1, R2, R3
Instruction cycle for an operate instruction:
Fetch | Decode | Execute | Memory

## Slide 6: Memory Access Instructions
Examples of memory access instruction:
LDR R1, R2, #2
STR R1, R2, #2
Instruction cycle for an operate instruction:
Fetch | Decode | Execute | Memory

## Slide 7: Registers vs Memory
Registers are “free”
  No additional memory access instruction
  Very fast to use, however, there are very few of them
Memory is expensive (slow), but very large
Notes: Desk analogy: books on your desk are registers. The library is memory

## Slide 8: Programmer View of CUDA Memories
Each thread can:
  Read/write per-thread registers (~1 cycle)
  Read/write per-block shared memory (~5 cycles)
  Read/write per-grid global memory (~500 cycles)
  Read/only per-grid constant memory (~5 cycles with caching)
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
Notes: Global, constant, and texture memory spaces are persistent across kernels called by the same application.

## Slide 9: Shared Memory in CUDA
A special type of memory whose contents are explicitly declared and used in the source code
  Located in the processor
  Accessed at much higher speed (in both latency and throughput)
  Still accessed by memory access instructions
  Commonly referred to as scratchpad memory in computer architecture

## Slide 10: CUDA Variable Type Qualifiers
__device__ is optional when used with __shared__, or __constant__
Automatic variables without any qualifier reside in a register
  Except per-thread arrays that reside in global memory
Variable declaration | Memory | Scope | Lifetime
int LocalVar; | register | thread | thread
__device__ __shared__ int SharedVar; | shared | block | block
__device__ int GlobalVar; | global | grid | application
__device__ __constant__ int ConstantVar; | constant | grid | application

## Slide 11: Where to Declare Variables?
Can host access it?
Outside of any Function
In the kernel
yes
no
global
constant
register (automatic)
shared
local

## Slide 12
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
1. __shared__ float ds_M[TILE_WIDTH][TILE_WIDTH];
2. __shared__ float ds_N[TILE_WIDTH][TILE_WIDTH];

## Slide 13: A Common Programming Strategy
Global memory resides in device memory (DRAM) - slow access
So, a profitable way of performing computation on the device is to tile input data to take advantage of fast shared memory:
  Partition data into subsets that fit into shared memory
  Handle each data subset with one thread block by:
    Loading the subset from global memory to shared memory, using multiple threads to exploit memory-level parallelism
    Performing the computation on the subset from shared memory; each thread can efficiently multi-pass over any data element
    Copying results from shared memory to global memory

## Slide 14: Matrix-Matrix Multiplication using Shared Memory

## Slide 15: Base Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
// Calculate the row index of the Pd element and M
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column idenx of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += d_M[Row*Width+k]* d_N[k*Width+Col];
d_P[Row*Width+Col] = Pvalue;
}

## Slide 16: How about performance on Fermi?
Grid
Global Memory
Block (0, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Block (1, 0)
Shared Memory
Thread (0, 0)
Registers
Thread (1, 0)
Registers
Host
Constant Memory
All threads access global memory for their input matrix elements
  Two memory accesses (8 bytes) per floating point multiply-add
  4B/s of memory bandwidth/FLOPS
  4*1,000 = 4,000 GB/s required to achieve peak FLOP rating
  150 GB/s limits the code at 37.5 GFLOPS
The actual code runs at about 25 GFLOPS
Need to drastically cut down memory accesses to get closer to the peak 1,000 GFLOPS

## Slide 17: Shared Memory Blocking Basic Idea
Thread 1
Thread 2
…
in
Global Memory
Thread 1
Thread 2
…
Global Memory
in
On-chip Memory

## Slide 18: Basic Concept of Blocking/Tiling
In a congested traffic system, significant reduction of vehicles can greatly improve the delay seen by all vehicles
  Carpooling for commuters
  Blocking/Tiling for global memory accesses
    drivers = threads,
    cars = data

## Slide 19: Some computations are more challenging to block/tile than others.
Some carpools may be easier than others
  More efficient if neighbors are also classmates or co-workers
  Some vehicles may be more suitable for carpooling
Similar variations exist in blocking/tiling

## Slide 20: Carpools need synchronization.
Good – when people have similar schedule
Bad – when people have very different schedule
Worker A
Worker B
Time
sleep
sleep
work
work
dinner
dinner
Worker A
Worker B
time
sleep
sleep
work
work
dinner
party

## Slide 21: Same with Blocking/Tiling
Good – when threads have similar access timing
Bad – when threads have very different timing
Thread 1
Thread 2
Time
Thread 1
Thread 2
time
…

## Slide 22: Outline of Technique
Identify a block/tile of global memory content that are accessed by multiple threads
Load the block/tile from global memory into on-chip memory
Have the multiple threads to access their data from the on-chip memory
Move on to the next block/tile

## Slide 23: Idea: Use Shared Memory to reuse global memory data
Each input element is read by WIDTH threads.
Load each element into Shared Memory and have several threads use the local version to reduce the memory bandwidth
  Tiled algorithms
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
ty
tx

## Slide 24: Work for Block (0,0) in a TILE_WIDTH = 2 Configuration
Col = 0 * 2 + threadIdx.x
Row = 0 * 2 + threadIdx.y
Col = 0
Col = 1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
Row = 0
Row = 1
blockIdx.x
blockIdx.y
blockDim.x
blockDim.y

## Slide 25: Tiled Multiply
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
Break up the execution of the kernel into phases so that the data accesses in each phase is focused on one subset (tile) of Md and Nd

## Slide 26: Loading a Tile
All threads in a block participate
  Each thread loads one Md element and one Nd element in based tiled code
Assign the loaded element to each thread such that the accesses within each warp is coalesced (more later).

## Slide 27: Work for Block (0,0)
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM
SM

## Slide 28: Work for Block (0,0)
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 29: Work for Block (0,0)
SM
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1

## Slide 30: Work for Block (0,0)
N1,0
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,1
SM

## Slide 31: Work for Block (0,0)
SM
M0,1
M0,0
M1,0
M0,2
M0,3
M1,1
M2,0
M2,2
M2,3
M2,1
M1,3
M1,2
M3,0
M3,2
M3,3
M3,1
N0,1
N0,0
N1,0
N0,2
N0,3
N1,1
N2,0
N2,2
N2,3
N2,1
N1,3
N1,2
N3,0
N3,2
N3,3
N3,1
P0,1
P0,0
P1,0
P0,2
P0,3
P1,1
P2,0
P2,2
P2,3
P2,1
P1,3
P1,2
P3,0
P3,2
P3,3
P3,1
M0,1
M0,0
M1,0
M1,1
N0,1
N0,0
N1,0
N1,1
SM

## Slide 32: Barrier Synchronization
An API function call in CUDA
  __syncthreads()
All threads in the same block must reach the __synctrheads() before any can move on
Best used to coordinate tiled algorithms
  To ensure that all elements of a tile are loaded
  To ensure that all elements of a tile are consumed

## Slide 33
Figure 4.11 An example execution timing of barrier synchronization.
…
Thread 0
Thread 1
Thread 2
Thread 3
Thread 4
…
Thread N-3
Thread N-2
Thread N-1
Time

## Slide 34: Loading an Input Tile
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
m
k
bx
by
k
m
Row = by * TILE_WIDTH +ty
Accessing tile 0 2D indexing:
M[Row][tx]
N[ty][Col]

## Slide 35: Loading an Input Tile
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
m
k
bx
by
k
m
Row = by * TILE_WIDTH +ty
Accessing tile 1 in 2D indexing:
M[Row][1*TILE_WIDTH+tx]
N[1*TILE_WIDTH+ty][Col]

## Slide 36: Loading Input Tile m
d_M
d_N
d_P
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
m*TILE_WIDTH
m*TILE_WIDTH
Col
Row
…
…
However, M and N are dynamically allocated and can only use 1D indexing:
M[Row][m*TILE_WIDTH+tx]
M[Row*Width + m*TILE_WIDTH + tx]
N[m*TILE_WIDTH+ty][Col]
N[(m*TILE_WIDTH+ty) * Width + Col]

## Slide 37: Tiled Matrix Multiplication Kernel
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
1. __shared__ float ds_M[TILE_WIDTH][TILE_WIDTH];
2. __shared__ float ds_N[TILE_WIDTH][TILE_WIDTH];
3. int bx = blockIdx.x; int by = blockIdx.y;
4. int tx = threadIdx.x; int ty = threadIdx.y;
// Identify the row and column of the Pd element to work on
5. int Row = by * TILE_WIDTH + ty;
6. int Col = bx * TILE_WIDTH + tx;
7. float Pvalue = 0;
// Loop over the Md and Nd tiles required to compute the Pd element
8. for (int m = 0; m < Width/TILE_WIDTH; ++m) {
// Coolaborative loading of Md and Nd tiles into shared memory
9. ds_M[ty][tx] = d_M[Row*Width + m*TILE_WIDTH+tx];
ds_N[ty][tx] = d_N[Col+(m*TILE_WIDTH+ty)*Width];
__syncthreads();
12. for (int k = 0; k < TILE_WIDTH; ++k)
13. Pvalue += ds_M[ty][k] * ds_N[k][tx];
14. __synchthreads();
15.}
16. d_P[Row*Width+Col] = Pvalue;
}

## Slide 38: Compare with the Base Kernel
__global__ void MatrixMulKernel(float* d_M, float* d_N, float* d_P, int Width)
{
// Calculate the row index of the Pd element and M
int Row = blockIdx.y*TILE_WIDTH + threadIdx.y;
// Calculate the column idenx of Pd and N
int Col = blockIdx.x*TILE_WIDTH + threadIdx.x;
float Pvalue = 0;
// each thread computes one element of the block sub-matrix
for (int k = 0; k < Width; ++k)
Pvalue += d_M[Row*Width+k]* d_N[k*Width+Col];
d_P[Row*Width+Col] = Pvalue;
}

## Slide 39: First-order Size Considerations
Each thread block should have many threads
  TILE_WIDTH of 16 gives 16*16 = 256 threads
  TILE_WIDTH of 32 gives 32*32 = 1024 threads
For 16, each block performs 2*256 = 512 float loads from global memory for 256 * (2*16) = 8,192 mul/add operations.
For 32, each block performs 2*1024 = 2048 float loads from global memory for 1024 * (2*32) = 65,536 mul/add operations

## Slide 40: Shared Memory and Threading
Each SM in Fermi has 16KB or 48KB shared memory*
  SM size is implementation dependent!
  For TILE_WIDTH = 16, each thread block uses 2*256*4B = 2KB of shared memory.
  Can potentially have up to 8 Thread Blocks actively executing
    This allows up to 8*512 = 4,096 pending loads. (2 per thread, 256 threads per block)
  The next TILE_WIDTH 32 would lead to 2*32*32*4B= 8KB shared memory usage per thread block, allowing 2 or 6 thread blocks active at the same time
Using 16x16 tiling, we reduce the accesses to the global memory by a factor of 16
  The 150GB/s bandwidth can now support (150/4)*16 = 600GFLOPS!
*Configurable vs L1, total 64KB

## Slide 41: Boundary conditions
What to do if the matrix size is not a multiple of width?
  Tricky problem, lets work through an example
Too many boundary checks can cause control divergence and overhead
Something that you have to work through for lab 2
  I’ll start a piazza discussion on the topic

## Slide 42: Device Query
Number of devices in the system
    int dev_count;
    cudaGetDeviceCount( &dev_count);
Capability of devices
    cudaDeviceProp dev_prop;
    for (i = 0; i < dev_count; i++) {
    cudaGetDeviceProperties( &dev_prop, i);
// decide if device has sufficient resources and capabilities
    }
cudaDeviceProp is a built-in C structure type
  dev_prop.dev_prop.maxThreadsPerBlock
  dev_prop.sharedMemoryPerBlock
  …

## Slide 43: Summary- Typical Structure of a CUDA Program
Global variables declaration
  __host__
  __device__... __global__, __constant__, __texture__
Function prototypes
  __global__ void kernelOne(…)
  float handyFunction(…)
Main ()
  allocate memory space on the device – cudaMalloc(&d_GlblVarPtr, bytes )
  transfer data from host to device – cudaMemCpy(d_GlblVarPtr, h_Gl…)
  execution configuration setup
  kernel call – kernelOne<<<execution configuration>>>( args… );
  transfer results from device to host – cudaMemCpy(h_GlblVarPtr,…)
  optional: compare against golden (host computed) solution
Kernel – void kernelOne(type args,…)
  variables declaration - auto, __shared__
    automatic variables transparently assigned to registers
  syncthreads()…
Other functions
  float handyFunction(int inVar…);
repeat
as needed

## Slide 44: Any more questions? Read Chapter 5!