## Slide 1: CS/EE 217 GPU Architecture and Parallel Programming Lecture 9: Tiled Convolution Analysis

## Slide 2: Objective
To learn more about the analysis of tiled algorithms

## Slide 3: If we used a larger (8 element) tile
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
For Mask_Width = 5, we load 8+5-1 = 12 elements (12 memory loads)
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 4: Each output P element uses 5 N elements (in N_ds)
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
P[8] uses N[6], N[7], N[8], N[9], N[10]
P[9] uses N[7], N[8], N[9], N[10], N[11]
P[10] uses N[8], N[9], N[10], N[11], N[12]
…
P[14] uses N[12], N[13], N[14], N[15],N[16]
P[15] uses N[13], N[14], N[15], N[16], N[17]
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 5: A simple way to calculate tiling benefit
(8+5-1)=12 elements loaded
8*5 global memory accesses replaced by shared memory accesses
This gives a bandwidth reduction of 40/12=3.3

## Slide 6: In General
Tile_Width + Mask_Width -1 elements loaded
Tile_Width * Mask_Width global memory accesses replaced by shared memory access
This gives a reduction of bandwidth by
(Tile_Width *Mask_Width)/(Tile_Width+Mask_Width-1)

## Slide 7: Another Way to Look at Reuse
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
N[6] is used by P[8] (1X)
N[7] is used by P[8], P[9] (2X)
N[8] is used by P[8], P[9], P[10] (3X)
N[9] is used by P[8], P[9], P[10], P[11] (4X)
N[10] is used by P[8], P[9], P[10], P[11], P[12] (5X)
… (5X)
N[14] is uses by P[12], P[13], P[14], P[15] (4X)
N[15] is used by P[13], P[14], P[15] (3X)
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 8: Another Way to Look at Reuse
The total number of global memory accesses (to the (8+5-1)=12 N elements) replaced by shared memory accesses is
1 + 2 + 3 + 4 + 5 * (8-5+1) + 4 + 3 + 2 + 1
= 10 + 20 + 10
= 40
So the reduction is
40/12 = 3.3

## Slide 9: Ghost elements change ratios
For a boundary tile, we load Tile_Width + (Mask_Width-1)/2 elements
  10 in our example of Tile_Width =8 and Mask_Width=5
Computing boundary elements do not access global memory for ghost cells
  Total accesses is 3 + 4+ 6*5 = 37 accesses
The reduction is 37/10 = 3.7

## Slide 10: In General for 1D
The total number of global memory accesses to the (Tile_Width+Mask_Width-1) N elements replaced by shared memory accesses is
1 + 2 + … + Mask_Width-1+ Mask_Width * (Tile_Width -Mask_Width+1) + Mask_Width-1+… + 2 + 1
= (Mask_Width-1) *Mask_Width+ Mask_Width*(Tile_Width-Mask_Width+1)
= Mask_Width*(Tile_Width)

## Slide 11: Bandwidth Reduction for 1D
The reduction is
Mask_Width * (Tile_Width)/(Tile_Width+Mask_Size-1)
Tile_Width | 16 | 32 | 64 | 128 | 256
Reduction Mask_Width = 5 | 4.0 | 4.4 | 4.7 | 4.9 | 4.9
Reduction Mask_Width = 9 | 6.0 | 7.2 | 8.0 | 8.5 | 8.7

## Slide 12: 2D Output Tiling and Indexin (P)
Use a thread block to calculate a tile of P
  Each output tile is of TILE_SIZE for both x and y
col_o = blockIdx.x * TILE_WIDTH + tx;
row_o = blockIdx.y*TILE_WIDTH + ty;

## Slide 13: Input tiles need to cover halo elements.
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
Output Tile
Input Tile
Mask_Width = 5

## Slide 14: A Simple Analysis for a small 8X8 output tile example
12X12=144 N elements need to be loaded into shared memory
The calculation of each P element needs to access 25 N elements
8X8X25 = 1600 global memory accesses are converted into shared memory accesses
A reduction of 1600/144 = 11X

## Slide 15: In General
(Tile_Width+Mask_Width-1) 2 elements from N need to be loaded into shared memory for each tile
The calculation of each P element needs to access Mask_Width 2 elements
  Tile_Width 2 * Mask_Width 2 global memory accesses are converted into shared memory accesses
The reduction is
Tile_Width 2 * Mask_Width 2 / (Tile_Width+Mask_Width-1) 2

## Slide 16: Bandwidth Reduction for 2D
The reduction is
Mask_Width 2 * (Tile_Width) 2 /(Tile_Width+Mask_Size-1) 2
Tile_Width | 8 | 16 | 32 | 64
Reduction Mask_Width = 5 | 11.1 | 16 | 19.7 | 22.1
Reduction Mask_Width = 9 | 20.3 | 36 | 51.8 | 64

## Slide 17: Ghost elements change ratios
Left as homewok.

## Slide 18: Any MORE QUESTIONS? Read Chapter 8