## Slide 1: What GPGPU-Sim Simulates
Functional model for PTX/SASS
  PTX = Parallel Thread eXecution
    A scalar low-level, data-parallel virtual ISA defined by Nvidia
  SASS = Native ISA for Nvidia GPUs
  Not DirectX, Not shader model N, Not AMD’s ISA, Not x86, Not Larrabee. Only PTX or SASS.
Timing model for the compute part of a GPU
  Not for CPU or PCIe
  Only model microarchitecture timing relevant to GPU compute
Power model for the compute parts
  Other parts idle when GPU is running compute kernels

## Slide 2: Functional Model (PTX)
Low-level, data-parallel virtual machine by Nvidia
  Instruction level
  Unlimited registers
  Parallel threads running in blocks; barrier synchronization instruction
Scalar ISA
  SIMT execution model
Intermediate representation in CUDA tool chain:
.cu
.cl
NVCC
OpenCL Drv
PTX
ptxas
G80
GT200
Fermi
Kepler

## Slide 3
for (int d = blockDim.x; d > 0; d /= 2)
{
__syncthreads();
if (tid < d) {
float f0 = shared[tid];
float f1 = shared[tid + d];
if (f1 < f0)
shared[tid] = f1;
}
}
$Lt_0_6146:
bar.sync 0;
setp.le.s32 %p3, %r7, %r1;
@%p3 bra $Lt_0_6402;
ld.shared.f32 %f3, [%rd9+0];
add.s32 %r9, %r7, %r1;
cvt.s64.s32 %rd18, %r9;
mul.lo.u64 %rd19, %rd18, 4;
add.u64 %rd20, %rd6, %rd19;
ld.shared.f32 %f4, [%rd20+0];
setp.gt.f32 %p4, %f3, %f4;
@!%p4 bra $Lt_0_6914;
st.shared.f32 [%rd9+0], %f4;
$Lt_0_6914:
$Lt_0_6402:
shr.s32 %r10, %r7, 31;
mov.s32 %r11, 1;
and.b32 %r12, %r10, %r11;
add.s32 %r13, %r12, %r7;
shr.s32 %r7, %r13, 1;
mov.u32 %r14, 0;
setp.gt.s32 %p5, %r7, %r14;
@%p5 bra $Lt_0_6146;
Scalar PTX ISA
Scalar control flow (if-branch, for-loops)
Parallel Intrinsic (__syncthreads())
Register allocation not done in PTX
// some initialization code omitted
Functional Model (PTX)
Notes: Shown kernel code = Parallel Reduction in CUDA
3

## Slide 4: Interfacing GPGPU-Sim to Applications
GPGPU-Sim compiles into a shared runtime library and implements the API:
  libcudart.so  CUDA runtime API
  libOpenCL.so  OpenCL API
Static Linking no longer supported.
Modify your LD_LIBRARY_PATH to run your CUDA app on GPGPU-Sim (See Manual)
  Need a config file (gpgpusim.config), an interconnection config file and a McPAT config as well
We provide the config files for modeling:
Quadro FX 5800 (GT200)
Geforce GTX 480 and Tesla C2050 (Fermi)

## Slide 5: GPGPU-Sim Runtime Flow
CUDA 3.1
CUDA 4.0 and Later

## Slide 6: Debugging and Visualization
GPGPU-Sim provides tools to debug and visualize simulated GPU behavior.
  GDB macros: Cycle-level debugging
  AerialVision: High-level performance dynamics
Notes: Microarchitecture simulator strength: Visibility  Allow deep understanding of performance

## Slide 7: Timing Model for Compute Parts of a GPU
GPGPU-Sim models timing for:
  SIMT Core (SM, SIMD Unit)
  Caches (Texture, Constant, …)
  Interconnection Network
  Memory Partition
  Graphics DRAM
It does NOT model timing for:
  CPU, PCIe
  Graphics Specific HW (Rasterizer, Clipping, Display… etc.)
GPU
PCIe
Interconnect
Gfx DRAM
Mem Part.
SIMT Cores
Cache
Raster…
Gfx HW
CPU

## Slide 8: Timing Model for GPU Micro-architecture
GPGPU-Sim simulates the timing model of a GPU running each launched CUDA kernel.
  Reports # cycles spent running the kernels.
  Exclude any time spent on data transfer on PCIe bus.
  CPU may run concurrently with asynchronous kernel launches.
Time
GPU HW
CPU
Async. Kernel Launch
Done
GPU HW
Done
CPU
GPU HW
Sync. Kernel Launch
Done
CPU
Blocking
GPGPU-Sim
GPGPU-Sim
GPGPU-Sim

## Slide 9: Timing Model for GPU Micro-architecture
GPGPU-Sim is a detailed cycle-level simulator:
  Cycle-level model for each part of the microarchitecture
  Research focused
    Ignoring rare corner cases to reduce complexity
  CUDA manual provides some hints. NVIDIA IEEE Micro articles provide other hints. In most cases we can only guess at details. Guesses “informed” by studying patents and microbenchmarking.
GPGPU-Sim w/ SASS is ~0.98 correlated to the real HW.

## Slide 10: Timing Model Overview
What is a warp?
SIMT Core Internals
  SIMT Frontend
  Memory Unit
Interconnection Network
Clock Domains
Memory Partition
  DRAM Timing Model

## Slide 11: Thread Hierarchy Revisited
SIMT Core
Recall, kernel = grid of blocks of warps of threads
Thread blocks (CTAs) contains up to 1024 threads
Threads are grouped into warps in hardware
Each block is dispatched to a SIMT core as a unit of work: All of its warps run in the core’s pipeline until they are all done.
Source: NVIDIA
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Thread Block
(CTA)
32 Threads
32 Threads
32 Threads
Warps
Notes: Remember that earlier when were talking about the CUDA programming model we mentioned the thread hierarchy. Each kernel launches a grid of thread blocks.
Blocks contain many threads, and each group of 32 threads is are grouped into warps in hardware.
11

## Slide 12: Warp = SIMT Execution of Scalar Threads
Warp = Scalar threads grouped to execute in lockstep
SIMT vs SIMD
  SIMD: HW pipeline width must be known by SW
  SIMT: Pipeline width hidden from SW (★)
Thread Warp 3
Thread Warp 8
Thread Warp 7
Thread Warp
Scalar
Thread
W
Scalar
Thread
X
Scalar
Thread
Y
Scalar
Thread
Z
Common PC
SIMT Pipeline
(★) Can still write software that assumes threads in a warp execute in lockstep (e.g. see reduction in NVIDIA SDK)
Notes: 12
In SIMD, you need to specify the data array + an instruction (on which to operate the data on) + THE INSTRUCTION WIDTH. Eg: You might want to add 2 integer arrays of length 16, then a SIMD instruction would look like (the instruction has been cooked-up by me for demo) add.16 arr1 arr2 However, SIMT doesn't bother about the instruction width. So, essentially, you could write the above example as: arr1[i] + arr2[i] and then launch as many threads as the length of the array, as you want. Note that, if the array size was, let us say, 32, then SIMD EXPECTS you to explicitly call two such 'add.16' instructions! Whereas, this is not the case with SIMT.

## Slide 13: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 14: Inside a SIMT Core
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Done (Warp ID)
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 15: Inside a SIMT Core (2.0)
Started from a 5-stage In-Order Pipeline
  Add fine-grained multithreading
  Add SIMT stacks
Schedule
+ Fetch
Decode
Register
Read
Execute
Memory
Writeback
Notes: As we learn more about the GPU design, we tried to add more detail to this model. At some point, we feel that we need to redesign from scratch.

## Slide 16: Inside a SIMT Core (3.0)
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Redesign Model
  Three decoupled warp schedulers
  Scoreboard
  Operand collector
  Multiple SIMD functional unit
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 17: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 18: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Round-Robin Priority
  GT200 (e.g. Quadro FX 5800): Allow dual issue
  Fermi: Odd/Even scheduler
For each issued instruction:
  Functional execution
  Obtain info from functional simulator
  Generate coalesced memory accesses
  Reserve output register in scoreboard
  Update SIMT stack

## Slide 19: Scoreboard
Checks for RAW and WAW dependency hazard
  Flag instructions with hazards as not ready in I-Buffer (masking them out from the scheduler)
Instructions reserves registers at issue
Release them at writeback

## Slide 20: SIMT Stack
A: v = foo[tid.x];
B: if (v < 10)
C: v = 0;
else
D: v = 10;
E: w = bar[tid.x]+v;
Time
Handles Branch Divergence
D
E
0011
C
E
1100
B
-
1111
PC
RPC
Active Mask
E
-
1111
A
T1
T2
T3
T4
B
T1
T2
T3
T4
C
T1
T2
D
T3
T4
E
T1
T2
T3
T4
SIMT Stack
foo[] = {4,8,12,16};
One stack per warp

## Slide 21: Operand Collector
Operand Collector Architecture (US Patent: 7834881)
  Interleave operand fetch from different threads to achieve full utilization
Bank 0
Bank 1
Bank 2
Bank 3
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
…
…
…
…
add.s32 R3, R1, R2;
No Conflict
mul.s32 R3, R0, R4;
Conflict at bank 0

## Slide 22: Operand Collector
(from instruction issue stage)
dispatch

## Slide 23: ALU Pipelines
SIMD Execution Unit
Fully Pipelined
Each pipe may execute a subset of instructions
Configurable bandwidth and latency (depending on the instruction)
Default: SP + SFU pipes

## Slide 24: Writeback
Each pipeline has a result bus for writeback
Exception:
  SP and SFU pipe shares a result bus
  Time slots on the shared bus is pre-allocated

## Slide 25: Memory Unit
Model timing for memory instructions
Support half-warp (16 threads)
  Double clock the unit
  Each cycle service half the warp
Has a private writeback path

## Slide 26
A Read-only cache for constant memory
GPGPU-Sim simulates 1 read ports
  A warp can access 1 constant cache locations in a single memory unit cycle
  If more than 1 locations accessed
    reads are serialized causing pipeline stalls
  # of ports is not configurable
Constant Cache

## Slide 27
Read-only cache with FIFO retirement
  Design based on Igehy et al. Prefetching in a Texture Cache Architecture, SIGGRAPH 1998.
GPGPU-Sim support 1-D and 2-D textures
2-D locality should be preserved when texture cache blocks are fetched from memory
  GPGPU-Sim uses a 4-D blocking address scheme to promote spatial locality in 2-D
    Based on Hakura et al. The Design and Analysis of a Cache Architecture for Texture Mapping, ISCA 1997
Texture Cache
Notes: 27

## Slide 28: Shared Memory
Explicitly managed scratchpad memory
  As fast as register files in absence of bank conflicts
Threads in a block can cooperate via shared memory
Each SIMT core has its own shared memory
  Dynamically allocated to thread blocks
16kB/48kB per SIMT core in current NVIDIA GPUs (Fermi)
Notes: 28

## Slide 29: Shared Memory (cont.)
Many threads accessing memory
  Therefore Shared memory is highly banked
Each bank serves one address per cycle
Multiple access to a bank in a single cycle cause bank conflicts
  Conflicting accesses must be serialized
Shared memory in NVIDIA GPUs has 16/32 banks
  Configurable in GPGPU-Sim (version 3.1.2)
Notes: Shared memory can be as fast as registers if there is no bank conflict if there is a bank conflict cost = max simultaneous accesses to the same bank.
29

## Slide 30: Shared Memory Bank Conflicts
No bank conflict
8-way bank conflict
Figures taken from CUDA manual by NVIDIA

## Slide 31: Global Memory
Global memory is the off-chip DRAM memory
  The largest and slowest memory available
  Accesses must go through interconnect, memory partition and off-chip DRAM
  Optionally cached in HW
    L1 Data Cache
    L2 Unified Cache
Notes: 31

## Slide 32: Coalescing
Combining memory accesses made by threads in a warp into fewer transactions
  E.g. if threads in a warp are accessing consecutive 4-byte sized locations in memory
    Send one 128–byte request to DRAM (coalescing)
    Instead of 32 4-byte requests
This reduces the number of transactions between SIMT cores and DRAM
  Less work for Interconnect, Memory Partition and DRAM
Notes: 32

## Slide 33: Coalescing (Cont.)
CUDA Capability 1.3 (e.g. GTX280)
  Coalescing done per half-warp
  Can create 128-byte, 64-byte or 32-byte transactions
CUDA Capability 2.0 (e.g. Fermi)
  Coalescing done for a full warp
  Cached: Only creates 128-byte transactions
  Not Cached: Can create 128/64/32-byte transactions
GPGPU-Sim supports both
Notes: 33

## Slide 34: Coalescing (cont.)
Coalescing example
Warp
Warp
One 128-Byte Transaction
Two 128-Byte Transactions
= 4-bytes in memory
Figures taken from CUDA manual by NVIDIA

## Slide 35: L1 Data Cache
For both local and global memory space
  With different policies
Non-coherent
Single ported (128-Byte wide)
  Takes multiple cycles to service non-coalesced accesses
 | Local Memory | Global Memory
Write Hit | Write-back | Write-evict
Write Miss | Write no-allocate | Write no-allocate
Notes: Reminder: Here we are referring to “Local Memory” as defined in CUDA. It corresponds to “Private Memory” in OpenCL.

## Slide 36: Memory Access Tracking
Cached access
  Miss Status Holding Registers (MSHR)
Non-cached access
  Encode warp, target register in request packet
  Memory Unit writes replied data directly to target request

## Slide 37: Miss Status Holding Registers
MSHRs keep track of outstanding memory requests
  keep track of threads, target registers, request addresses
GPGPU-Sim: Each cache has its set of MSHRs
Each MSHR contains one or more memory requests to the same address
  MSHRs are limited (configurable)
  Memory unit stalls if cache runs out of MSHRS
One approach that might make sense
  No details available from NVIDIA / AMD
Notes: 37

## Slide 38: Atomic Operations
Both CUDA and OpenCL support atomic operations
  Read-modify-write on a single memory location
Coalescing rules ~ global memory access
  Put accesses to same memory location in separate transactions
GPGPU-Sim simulate these as:
  Load operations inside a SIMT core
    Skips L1 data cache
  Store operations at memory partition

## Slide 39: SIMT Core Model (Fermi Architecture)
Just a configuration in our model

## Slide 40: SIMT Core Cluster
Collection of SIMT cores

## Slide 41: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 42: Clock domains
Simulate independent clock domains for
  SIMT cores
    GT200: Set to ¼ of shader clock to compensate for using SIMD width of 32 instead of 8
    Fermi: Set to ½ of shader clock to compensate for using SIMD width of 32 instead of 16
  Interconnection network
  L2 cache (if enabled)
  DRAM
    This is real clock (command clock)
    Effective clock is 2x this clock due to DDR
Notes: 42

## Slide 43: Clock Domain Crossing
We simulate send and receive buffers at clock crossing boundaries
The buffers are filled and drained in different clock domains
E.g. consider the buffer from interconnect to memory partition
  Filled at interconnect clock rate
  Drained at DRAM clock rate

## Slide 44: Interconnection Network Model
Intersim (Booksim) a flit level simulator
  Topologies (Mesh, Torus, Butterfly, …)
  Routing (Dimension Order, Adaptive, etc. )
  Flow Control (Virtual Channels, Credits)
We simulate two separate networks
  From SIMT cores to memory partitions
    Read Requests, Write Requests
  From memory partitions to SIMT cores
    Read Replies, Write Acks
Notes: 44

## Slide 45
Topology Examples
Notes: There are a diverse range of topologies that can be used to transfer memory requests in a many-core architecture.
In Nvidia’s GPUs, it looks something like a crossbar except multiple SIMT cores share input ports.
Intel’s Larrabee looks like a ring.
In our ISPASS paper we found that a mesh was viable as well.
45

## Slide 46: Interconnection Network Config
Booksim has its own config file
  Topology (topology, k ,n )
  Virtual channels (num_vcs)
  Buffers per VC (vc_buf_size)
  Routing (routing _function)
  Speedups (input_speedup, internal_speedup)
  Allocators (vc_allocator, sw_allocator)
Specific to GPGPU-sim
  Channel Width (flit_size)
  Setting memory partition locations (use_map)
Notes: 46

## Slide 47: Interconnect Injection Interfaces
Clock Boundary
SIMT Core
Router
Core Clock Domain
Interconnect Clock Domain
1 Flit / Cycle
1 Packet / Cycle

## Slide 48: Interconnect Injection Interfaces
Clock Boundary
Memory Partition
Router
DRAM Clock Domain
Interconnect Clock Domain
1 Flit / Cycle
1 Packet / Cycle

## Slide 49: Interconnect Injection Interfaces
Clock Boundary
L2 Cache
Router
L2 Clock Domain
Interconnect Clock Domain
1 Flit / Cycle
1 Packet / Cycle

## Slide 50: Interconnect Ejection Interfaces
1 Ejection/boundary buffer per VC (1 flit / cycle)
A credit is sent back to router as a flit goes from ejection to boundary buffer
Clock Boundary
Router
SIMT
Core
Core Clock Domain
Interconnect Clock Domain
Ejection Buffers
Boundary Buffers
Credit return buffer
1 Credit / Cycle
1 Flit / Cycle
1 Flit / Cycle
1 Packet / Cycle
(Round Robin)
# of VCs
Notes: We have one ejection buffer and one boundary buffer for each VC.
Why? If all VCs share the same set of buffers then the flits from different packet get mixed together so when
SIMT core tries to pop a packet per cycle and remove its corresponding flits from the buffer the flits are not together.
Also for each VC there is one ejection buffer and one boundary buffer. The reason for this is that we need to send a credit back to the router as a flit gets out of the ejection buffer. If we only had a single buffer then the interconnect would be forced to operate at Shader core domain since credits would be sent when the shader pops the packet. So to isolate the clock domains we have two buffers. In this design a credit is sent back to router as a flit goes from ejection to boundary buffer.
50

## Slide 51: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 52: Memory Address Mapping
Off-chip memory partitioned among several memory partitions
  GT200 has 8 memory partitions
  G80 and Fermi had 6 memory partitions
  Each memory partition has a DRAM controller
Successive 256-byte regions of memory are assigned to successive memory partitions
  Address mapping is configurable in GPGPU-Sim
UNSW CUDA Tutorial by NVIDIA part 4 optimizing CUDA
Notes: 52

## Slide 53: Mem. Address Mapping (Cont.)
0x0000
0x0100
0x0200
0x0300
0x0400
0x0500
0x0600
0x0700
0x0800
Memory
Partition 0
Memory
Partition 1
Memory
Partition 2
Memory
Partition 3
Memory
Partition 4
Memory
Partition 5
Memory
Partition 6
Memory
Partition 7
Interconnection Network
SIMT
Core
SIMT
Core
SIMT
Core
53
December 2009
GPGPU-Sim Tutorial (MICRO-42)

## Slide 54: Memory Partition
Service memory request (Load/Store/AtomicOp)
  Contains L2 cache bank, DRAM timing model
  Model Raster Operations Pipeline (ROP) latency

## Slide 55: L2 Cache Bank
GT200: Caches only texture
Fermi: Caches All memory spaces
Similar to L1 Data Cache
Missed requests are sent to DRAM
 | Local Memory | Global Memory
Write Hit | Write-back | Write-back
Write Miss | Write-allocate | Write-allocate
Notes: Reminder: Here we are referring to “Local Memory” as defined in CUDA. It corresponds to “Private Memory” in OpenCL.

## Slide 56: DRAM
DRAM Memory
  Off-chip, high-density and high capacity
DRAM access time is Not constant
  It has non-uniform access latencies
That’s why we model it!
Notes: 56

## Slide 57
DRAM
Column Decoder
Memory
Array
Row Decoder
Memory
Controller
Row Buffer
Row Buffer
Row Decoder
Column Decoder
Row Buffer
Column Decoder
Row Buffer
DRAM Access
Row access
  Activate a row or page of a DRAM bank
  Load it to row buffer
Column access
  Select and return a block of data in row buffer
Precharge
  Write back the opened row into DRAM
  Otherwise it will be lost!
Notes: Accessing data in DRAM consists of three steps: precharge, row access, and column access. A row access activates a page of data in the core and transfers it to the row buffer. After that, the column access selects the desired block and transfers it to the processor through the data bus.
57

## Slide 58: DRAM Row Access Locality
tRC = row cycle time
tRP = row precharge time
tRCD = row activate time
Notes: row access locality of a memory request stream is crucial to performance.
Within a bank, you have thousands of rows of data.
Before you can access a particular row, you have to load the row into the row buffer.
The time to close the previous row and open the new row is governed by the DRAM spec, and it can be a dominating factor in performance when there are few accesses per row, or low row access locality
58

## Slide 59
DRAM Bank-level Parallelism
To increase DRAM performance and utilization
  Multiple banks per DRAM chip
To increase bus width
  Multiple chips per Memory Controller
Notes: 59
You may have several chips connected in parallel to a controller to increase the bus width and the peak throughput.
Within a chip, you also have multiple banks to exploit bank-level parallelism. What this means is having multiple banks share the data bus to maximize utilization. If one bank is in the middle of switching rows, another bank can transfer data.
The BLP of memory request stream of an application is crucial to performance.
If you only use a single bank in a chip, any time it’s busy switching rows, that’s wasted data bus cycles.

## Slide 60
Scheduling DRAM Requests
Scheduling policies supported
    First in first out (FIFO)
      In-order scheduling
    First Ready First Come First Serve (FR-FCFS)
      Out of order scheduling
      Requires associative search

## Slide 61: Session Summary
Microarchitecture Timing Model in GPGPU-Sim
  SIMT Core
  Cache Model
  Interconnection Network
  Memory Partition + Address Mapping
  DRAM Scheduling and Timing